# Echo Link Codes

## The Echo Link web site is http://www.echolink.org/

To see the list of available stations and node numbers, down load the software and register.

The link to our repeater is N2QPD-R, node number 158772

## The following codes entered through the main repeater will control the echolink features.

Listen first to make sure the frequency is clear before bringing up the link.

Wait approx. 2 sec after keying up the repeater before entering codes.

Do not enter the codes too fast.

*	Before entering any codes, IDENTIFY.

*	IDENTIFY YOURSELF after making the connection, Echolink will ID the Link as N2QPD as it connects and disconnects.

- Due to the inherent time delays in the system you MUST wait 1-2 seconds before speaking after pressing your PTT.

REPEATER CODES ( Main Repeater PL 136.5 )

# CODES

**50	link up	Turns on Echolink. Will now accept connect codes to other stations.

After the confirmation that echolink has been enabled

You can then enter the node number you wish to connect to.

You must enter ** before the Node Number.

Or ,you can enter one of the following codes…

**01	Connect to Random Link

**00	Connect to Random Node

**03	Connect to Random User

** #	Disconnect from last connection. (Link will automatically drop after 5 minutes

of inactivity.)

**09	Reconnect to last connection.

**##    Disconnect from all connections if in conference.

**08	Link status

**51	link down	Turns off Echolink

Note : The “**” before the number is part of the code and must be entered.!

If you turn the link on, please make sure you turn it off  after the QSO.

# This is especially true if the link is used before a net. If the link is on,other

stations can call into the system and interrupt the net.

SEE PAGE 2 FOR INFO ON USING THE AUXILLARY REPEATER WITH ECHOLINK

# When using the Auxiliary repeater DO NOT use the ** prefix before the code.

The codes are the same but the ** is not used.

# REPEATER CODES ( AUX  Repeater PL 110.9 )

# CODES

50	link up	Turns on Echolink. Will now accept connect codes to other stations.

After the confirmation that Echolink has been enabled

You can then enter the node number you wish to connect to.

Or, you can enter one of the following codes…

01	Connect to Random Link

00	Connect to Random Node

03	Connect to Random User

#	Disconnect from last connection. (Link will automatically drop after 5 minutes

of inactivity.)

09	Reconnect to last connection.

##        Disconnect from all connections if in conference.

08	Link status

51	link down	Turns off Echolink

.